## Slide 1
NETWORK SETUP
vivi.io
Notes: Cover 2 Option

## Slide 2
NETWORK CONFIGURATION
To enable streaming across platforms, a few network ports must be open. Standard internet access is required for features such as Play Content which allows streaming from services like YouTube or ClickView (if configured).
Vivi supports multiple authentication sources, including Active Directory (LDAP or SAML) and Google OAuth. Some additional setup may be required depending on your choice.

## Slide 3
Firewall Exception
To connect to Vivi Central, the Vivi Box needs specific firewall exceptions. Many networks require these exceptions to ensure smooth operation.
You can check the Status page in the Web Console to see if Vivi has the necessary internet access.
Easiest Option: Add a Wildcard Exception
*.vivi.io (HTTP and HTTPS)
If Wildcards Can’t Be Used, Add These Exceptions Explicitly:
api.vivi.io (HTTP & HTTPS)
storage.vivi.io (HTTPS)
downloads.vivi.io (HTTPS)
In the rare case this list changes, we’ll notify you through a Service Announcement.
⚠️ Note: These exceptions must be added manually. Firewalls that allow browser traffic on ports 80 and 443 may still block Vivi, as it makes application-level connections.
Whitelisting the associated IP addresses of these hosts is not recommended, as they may change without warning. This is done at the user's own risk.
Additionally, some third-party security services and proxies may require that you also allow
• *.vivi-box.io
Notes: SECTION SLIDE PURPLE

## Slide 4
Opening Internal Ports
These ports are only needed on your LAN (not externally).
NETWORK CONFIGURATION
If your network uses multiple subnets or VLANs, open them between the relevant networks.
For Multi-Display or Combined Rooms, allow ports between Vivi Boxes.
These terms are described in more detail in the definitions section.
Vivi requires these ports and the Return Traffic ports to operate. Below, you'll find a list of these ports along with descriptions of their respective purposes.
Port
Protocol
Purpose
The following ports are all required to be opened between your end user devices (e.g. laptops) and Vivi Boxes for Vivi to work.
6000
TPC
Apple AirPlay negotiation, Video stream fallback
7000
TPC
Apple AirPlay negotiation
7100
TPC
Video Stream
8000
TPC
Apple AirPlay negotiation
Required Functional Ports
8001
UDP
Apple AirPlay timing channel
8002
UDP
Control messages , Live Broadcast (Video stream)
8003
UDP
Audio stream, Live Broadcast audio, WebRTC (full screen only)
12800
TCP
Vivi Client API – device communication, touch input
12801
TCP
Static image serving, Apple AirPlay fallback
12802
TCP
Local files streamed to the Box

## Slide 5
Port
Protocol
Purpose
These ports are not required for users to access Vivi, but instead will be used by IT Admins. Some are optional (see details below).
80
TPC
Web Console (HTTP), Bulk Config via Vivi Central
Administration Ports (IT Admin use only)
Port
Protocol
Purpose
These ports are also required to be opened in order to use the Video Announcements feature.
3001
TPC
Video Announcements
Video Announcements
161
UDP
SNMP diagnostics (optional)
443
TCP
Web Console (HTTPS), Bulk Config
5001
TCP
iPerf – bandwidth testing (by Vivi Support)
12819
TPC
WebRTC signalling
12821–12824
UDP
Video/audio streams
12820–13999
UDP
Inbound video/audio streams from broadcasting device
This additional port range must also be opened to use WebRTC Split Screen functionality
WebRTC Split Screen
12820–12836
UDP
Video/audio streams
This additional port range must be opened to use the Stream to Students functionality
Stream to Students
40001–40100
UDP
Video/audio streams

## Slide 6
Video Announcements
Our improved Video Announcements feature uses RTCP (Real-Time Transport Control Protocol) to monitor the performance of the audio and video streams and to quickly deal with problems like lost packets. This results in a much smoother and reliable experience when making a Video Announcement. To support RTCP, each Vivi box that is receiving the Video Announcement needs to make 2 UDP connections (1 for audio, 1 for video) to the client. This means if you are making a Video Announcement from your client to 10 boxes, your computer will receive a total of 20 inbound UDP connections. The large inbound UDP range here makes it possible to broadcast a Video Announcement to a large number of Vivi boxes simultaneously

## Slide 7
OPENING INTERNAL PORTS
Port Range: 49152–65535
Used by client devices to establish and maintain outbound connections.
Firewall Exceptions
Return Traffic (Ephemeral Ports)
Ensure:
• Outbound traffic from this range is allowed.
• Inbound return traffic is permitted for established sessions.
Testing Ports
To confirm configuration:
Log in to the Vivi App on a device.
01
Connect to a room.
02
Go to Settings > Room Settings > Port Check.
03
Results appear on the connected display.
04

## Slide 8
SSO Configuration
Vivi provides its own internal authentication source, and supports several different authentication types:
Microsoft Entra ID (Formerly Azure AD)
Google Workspace Integration
ClassLink
Clever
SSO Subdomain
LDAP/Secure LDAP Authentication
SAML
⚠️ Important: Enabling an external authentication source disables Vivi standard authentication. If IT Admin accounts are not mapped in the new source, they will lose access.
To configure:
In Vivi Central, select Organisation > Authentication.
Choose the desired authentication type.
Click Edit, apply settings, then Save Changes.
Notes: SECTION SLIDE PURPLE

## Slide 9
By default, Vivi uses its own built-in authentication system. This means:
User accounts are created and managed directly in Vivi Central.
Teachers and students can also download the Vivi App and sign up for an account themselves.
This method is best suited for smaller schools or trial environments because it requires minimal setup.
Firewall Exceptions
Vivi Standard Authentication (default)
To view or edit the current setting:
Go to Organisation in Vivi Central.
Select Authentication
To change settings click Edit > Select Vivi as the Authentication Type.
Click ”Save Changes” to confirm the changes.

## Slide 10
You can enable email confirmation to prevent fake or unauthorised sign-ups.
When enabled, users must verify their account by clicking a link sent to their email before gaining access.
This applies only when using Vivi Standard Authentication.
Firewall Exceptions
Email Confirmation
OPTIONAL SETTINGS
To stop external users from registering, you can restrict sign-ups to specific domains (e.g., school.edu.au).
Only users with an approved domain can create an account.
Allowed Email Domains
To manage:
Go to Organisation in Vivi Central.
Select Authentication
Click Edit Email Domains…
Use the ”+“ symbol to add new domains.
Use the ”–“ symbol to remove domains no longer required.
Click Update to save.
Note: If you add a top-level domain, users can register with any subdomain automatically.

## Slide 11
Presenters have full access to all features in the Vivi App.
With Standard Authentication, a Presenter Code is required at sign-up to assign this role.
Firewall Exceptions
Presenter Code
OPTIONAL SETTINGS
To set:
Go to Organisation > Details > Edit in Vivi Central.
Enter the code in the Presenter Code box.
Save changes.
Codes can include letters, numbers, symbols, and spaces.
If your school uses an external authentication method (e.g., Active Directory, Google, SAML), the Presenter role is managed via groups instead of a code.

## Slide 12
Wi-Fi Best Practices
Objective:
To ensure consistent and high-quality performance of the Vivi Box in a classroom environment by optimising Wi-Fi connectivity and maximising Signal-to-Noise Ratio (SNR). This will improve bandwidth throughput and reduce latency, ensuring a smooth and effective screen-sharing experience.
1. Understand SNR Benchmarks:
Good (>40 dBm): Optimal Wi-Fi connection; excellent experience even with high-bandwidth video content.
Average (25-40 dBm): Adequate connection; some minor jitter may occur with high-bandwidth content.
Poor (<25 dBm): Suboptimal connection; reduced resolution and framerate, leading to a poor user experience.
2. Optimize Vivi Box Placement:
Centralise Placement: Position the Vivi Box centrally in the classroom to minimise the distance between laptops and the Wi-Fi Access Point (WAP). This helps in achieving better signal strength.
Elevate and Clear Line of Sight: Place the Vivi Box at an elevated height (4-6 feet) and ensure it has a clear line of sight to connected devices to avoid physical obstructions and interference.
Avoid Obstacles: Keep the Vivi Box away from large metal objects, thick walls, and other electronic devices that could obstruct or degrade the Wi-Fi signal.

## Slide 13
Wi-Fi Best Practices
3. Improve Wi-Fi Network Configuration:
WAP Placement: Place the WAP(Wireless access point) in a central location, ideally elevated, to ensure even coverage across the classroom.
Use 5 GHz Band: Connect the Vivi Box to the 5 GHz band for better performance and reduced interference compared to the 2.4 GHz band. Ensure the WAP supports dual-band.
Optimize Channels: Configure the WAP to use the least congested Wi-Fi channel. Use a Wi-Fi analyser tool to select the optimal channel with minimal interference.
Static/Dynamic IP Address: Assign a static IP address or reserve a IP using DHCP reservation to the Vivi Box to ensure stable and consistent connectivity.
4. Monitor and Manage Signal Strength:
Check SNR Regularly: Use Vivi Central to monitor both current and historical SNR data for the Vivi Box. Aim for an SNR greater than 40 dBm for optimal performance.
Adjust Placement as Needed: If the SNR falls below the optimal range, adjust the placement of the Vivi Box or WAP to improve signal quality.
Minimise Interference: Identify and reduce potential sources of interference, such as other wireless devices, microwaves, or Bluetooth devices. Regularly check for new sources of interference.
5. Network and Device Maintenance:
Firmware Updates: Keep the Vivi Box and WAP firmware up-to-date to benefit from performance improvements and security patches.
Quality of Service (QoS): Configure QoS settings on the WAP to prioritize traffic for the Vivi Box, ensuring that screen-sharing performance is maintained even with other network activities.
Periodic Reviews: Regularly review network performance and SNR data to ensure that the setup continues to meet the required benchmarks and adjust configurations or placements as necessary.

## Slide 14
User Onboarding
Vivi provides a full suite of training options to ensure users are equipped to make the most of all the features:
In-person training
Our National Trainer is Melbourne based and can attend metro locations for in-person training including Train the Trainer sessions.
Online training sessions can also be arranged.
Vivi Training Hub
Teacher Guides
Training Videos
Vivi’s 3 levels of training courses for the classroom
Digital Signage training course
Tech Experts and IT Admins training course
Guides for Vivi App set up, Screen Sharing, Play Content & Student Engagement.
Guides for Campus Communications
Vivi YouTube Channel
Vimeo training videos
Notes: SECTION SLIDE PURPLE

## Slide 15
THANK YOU
vivi.io
Notes: Thank you slide (Do not edit)