## Slide 1
VIVI INITIAL SETUP
vivi.io
WELCOME TO THE
Notes: Cover 2 Option

## Slide 2
What’s Inside the Box?
Meet the Vivi Box
GETTING STARTED
A single solution for wireless screen mirroring and at-school communications.
Purpose-built for education, Vivi is completely device- and operating system-agnostic.
This little blue box is the key to connecting any device or media to any display.
To make your classroom Vivi-enabled, each display needs one of these boxes, all managed through our cloud-based admin platform.
Vivi Box
Power supply (AC adapter)
2 x Wi-Fi antennas
Mounting plate with screw kit (Kensington lock compatible)

## Slide 3
Connections
Meet the Vivi Box
GETTING STARTED
The Vivi Box connects directly to your display and takes care of all communication between devices and what’s shown on the screen.
What You’ll Need:
HDMI cable
Ethernet cable
Wi-Fi Antennas
AUX
HDMI
DC in
4x USB Ports
Reset Button (accessible with a pin)
Ethernet (POE enable)

## Slide 4
Organisation Setup
VIVI CENTRAL SETUP
If your school already has an organisation setup, you’re good to go! If not, no worries—our IT team will create one for you during the technical setup call.
Once your Vivi is set up, you’ll be ready to start using and managing it. But first, make sure to complete the following quick steps to get everything running smoothly.

## Slide 5
Plugging your device
FIRST TIME
TV Displays
Projectors
HDMI
HDMI
RJ45 / Ethernet Cable
Router
Vivi Box
Notes: SECTION SLIDE PURPLE

## Slide 6
TWO OPTIONS
Powering your Vivi Box
Once your Vivi Box is plugged in, it will boot up automatically. But before that, make sure all your other connections are in place.
You have two options for powering the Box:
AC Power Adapter (included in your kit)
Power over Ethernet (PoE) (requires roughly 15 watts of power)
Important: If you plan to connect the Box to Wi-Fi, you must use the AC adapter. Not all networks provide power through Ethernet, so check your setup.
Power Check:
If the power is working, you’ll see a red light near the power connection.
For new Boxes, the first boot might take a few minutes while the operating system sets up—just wait for the red light!

## Slide 7
FINAL STEPS
Get your Vivi Box ready!
After startup, you’ll see the Vivi logo and either the Box name or the room name on the display. Don’t worry if the screen flickers for a few seconds—this is normal while the device finishes installation and activation.

## Slide 8
FINAL STEPS
Next Steps
Allocate the Box to a room in Vivi Central to gain full access.
Network Configuration: Make sure to add the necessary firewall exceptions and open the required internal network ports. Once that's done, disconnect and reconnect the power so the box can reboot and complete the activation process.

## Slide 9
Firewall Exceptions for Vivi
To connect to Vivi Central, the Vivi Box needs specific firewall exceptions. Many networks require these exceptions to ensure smooth operation.
You can check the Status page in the Web Console to see if Vivi has the necessary internet access.
Easiest Option: Add a Wildcard Exception
*.vivi.io (HTTP and HTTPS)
If Wildcards Can’t Be Used, Add These Exceptions Explicitly:
api.vivi.io (HTTP & HTTPS)
logstash.vivi.io (HTTP)
storage.vivi.io (HTTPS)
downloads.vivi.io (HTTPS)
In the rare case this list changes, we’ll notify you through a Service Announcement.
Important: These must be added explicitly. Network administrators sometimes assume that these ports (80 and 443) are open by default for application traffic, but that’s not the case—these ports are usually open only for browser traffic.

## Slide 10
Opening Internal Ports for Vivi
For Vivi to work smoothly, you’ll need to open the following ports between your user devices (like laptops) and Vivi Boxes.
Required Functional Ports:
TCP: 6000, 7000, 7100, 8000, 12800, 12801, 12802
UDP: 8001, 8002, 8003
Using Multi-Display or Combined Rooms? These ports also need to be opened between Vivi Boxes (within the VLAN).
Using WebRTC Split Screen? Open this additional port range:
UDP: 12820 - 12836
Administration Ports: These ports are for IT admins:
TCP: 80, 443, 5001 (optional)
How to perform a port test? For more information click here.
Video Announcements: These ports are also required to be opened in order to use this feature:
TCP: 3001, 12819 (WebRTC Signaling)
UDP: 12821-12824 (Video & Audio Streams) 12820-13999 (Video & Audio Streams) This port range is required to be open inbound on the broadcasting device*

## Slide 11
Turn off the power, wait 10 seconds, and turn it back on. The Box will take about 20 seconds to boot up.
Using a device that can connect to Wi-Fi, join the temporary Wi-Fi network from the Box, named something like "Vivi-000000". Password: v!v!adm!n
Connect to the Vivi Box Hotspot:
01
Power Cycle the Box:
Open a browser and go to http://192.168.123.1 to access the Vivi’s web console.
Go to the Network Settings tab.
Set Wi-Fi as the primary configuration.
Tick “Enter Manually” under SSID and type the name of your home Wi-Fi.
Enter your Wi-Fi password in the pre-shared key field.
Configure the Wi-Fi Settings:
Access the Web Console:
After saving, reconnect to the same Wi-Fi network as the Vivi Box. If you can access the Web Console again, the setup was successful!
Save and Reconnect:
CONNECTING
Your Vivi box via Wi-Fi
02
03
04
05

## Slide 12
Configuring Your Vivi Box via the Web Console
The Web Console is an easy-to-use admin website where you can make configuration updates to your Vivi Box. It also lets you check the Box’s status and perform basic tasks like restarting the Box or sending logs to Vivi Support—just like the admin pages on most routers.
Key Features:
Each Vivi Box has its own Web Console.
A simple menu on the left guides you through configuration and admin tasks.
Access it by connecting to the Box’s IP address or its built-in Wi-Fi access point.
Login Details:
Username:
Password:
v!v!adm!n
admin

## Slide 13
YOUR VIVI BOX
Troubleshooting
Vivi Box Not Powering On
No red light? The Box has no power.
Check that the power adapter is securely plugged into both the outlet and the Box, and that the outlet is on.
Make sure you’re using the correct power adapter that came with the Box (or a compatible one).
Try another compatible power adapter if available. If it works, the original may be faulty.
If still no power, the Box itself could be faulty.
Nothing Shown on Display
Check that the display is set to the correct HDMI input.
Try all HDMI inputs if the display has more than one.
Swap the HDMI cable to rule out a faulty one.
And don’t forget: Make sure the display is turned on!
Can't See or Connect to Wi-Fi Hotspot
Restart the Box by unplugging and plugging it back in.
Ensure your device’s Wi-Fi adapter is working properly.
Unable to Connect to the Web Console
Double-check the IP address: Use http://192.168.123.1 when connected to the Box’s Wi-Fi hotspot.
Use the correct Box IP address on a normal network.
Ensure both the Box and your device are on the same network and that your device can ping the Box's IP.
HTTP/HTTPS Access Issues
HTTP Access: Make sure network configuration steps (firewall exceptions, static IP, proxy settings) are correct.
Click "Show Details" next to HTTP access on the Web Console Status page for more info.
HTTPS Access: Check that the correct time is displayed on the Web Console Status page. If not, press "Set Time To Now."

## Slide 14
Useful Information
Firewall Exceptions
Internal Ports
Enterprise Client Downloads
Network Settings
Book your technical setup call here
vivi.io/get-started

## Slide 15
THANK YOU
vivi.io
Notes: Thank you slide (Do not edit)